# Band Saw

## Teacher Reference Page

Recommended Level(s) of use/Supervision

High School 		Independent student use (with permission)

Middle School	Independent student use (with permission)

Elementary 		Teacher use only

Notes:

- High School instructors may want to grant generic use permission for the band saw to advanced students who have consistently demonstrated safe operating techniques on the band saw.

- Instructors may want to add additional items that are specific references to unique machines or circumstances in their specific lab. (ie. the use of a brake if applicable, or a differentiation between machines ie. the 14” band saw –vs- the 20” band saw)

- Instructors need to define the safety zone for the band saw in their lab.

  - A  2’ to 3’ clearance would be appropriate.

  - Safety zones for stationary equipment must be marked with safety tape on the floor if a stationary machine is used. (Safety tape is available through the Career & Technology Office).

  - If portable, students should be acutely aware of what area the safety zone encompasses, i.e., the length of two floor tiles.

- There is a radius chart with some excellent everyday references regarding blade size –vs.- cutting radius included on page 4.

# Band Saw

### Safety Rules

- Permission must be obtained from the instructor before using the band saw!

- Always wear Safety Glasses when operating the band saw!

- Always remove jewelry, eliminate loose clothing and tie back long hair before operating the band saw.

- Never talk to anyone while operating the band saw.

- No one should be within the safety zone while you are operating the band saw.

- The blade guide assembly must be adjusted to within ¼” of the work piece before turning the saw on.

- Round stock must be secured before cutting.

- Relief cuts are necessary when cutting curves smaller then the blade allows.

- You should Always avoid backing out of curves or long straight cuts with the saw running.

- Never place your hands or fingers directly in line with the blade.

- Never force the work into the blade

- Never allow anyone to stand to the right of the saw when it is running. (When blades break, they may shoot out that side of the saw)

- If the saw makes a strange noise, turn off the power and inform the instructor.

- If the blade breaks, turn off the power, wait until the machine stops completely and then inform the instructor.

- Never remove scraps from near the blade until the blade has come to a complete stop.

- Never leave the band saw until the blade has come to a complete stop.

# Band Saw

### Operating Procedure

- Ask the instructor for permission before using the band saw.	Always wear safety glasses.

- Remove loose clothing and jewelry, tie back long hair and roll up long sleeves.

- Check set-up, operation, and adjustments before turning on the saw.

- Adjust blade guide assembly to within ¼” of the work piece

- Check that both door guards are in place and secure.

- Do not allow anyone inside the safety zone.

- Do not talk to anyone while operating the band saw.

- Turn the saw on.

- Place hands and fingers on each side of the cut line. Never allow your fingers or hands to be in line with the blade.  Use a push stick if necessary.

- Guide the work slowly, letting the machine do the work.  Do not force the work into the cut.

- Avoid backing out of long cuts or curves with the saw running.

- Use relief cuts if they are needed for sharp curves.

- If any strange noise is heard, immediately shut off the machine and inform the teacher.

- If the blade breaks, turn off the power, step back from the machine, wait until it stops and notify the instructor.

- Turn the saw off.

- Wait until the blade comes to a complete stop before removing any wood that is close to the blade.

- Do not leave the band saw until the blade has come to a complete stop.

Using a Radius Chart

Until you become well acquainted with your saw, it is best to use the contour (radius) chart shown in “Figure 6-6” to determine which size blade to use for a specific application.  Radius charts can be found in many woodworking books, magazine articles and on blade boxes.  They differ slightly from one another, but are good as rough indicators of how tightly a curve can be cut with a particular blade.  Each blade, saw and operator are different, so it is impossible to make a truly accurate chart.

A blade can cut continuously without backtracking any curve that has a radius as much as or more than that shown on the chart.  For example, a 3/16” blade will cut a circle with a 5/16” radius or a 5/8” diameter.  To test if a 3/16” blade would work for a particular curve, place a dime, which is roughly 5/8”, over the pattern.  The 3/16”’ blade can cut a curve bigger than the dime, but not smaller.

You can use everyday items such as coins or a pencil to determine which blade to use.  A quarter is the size of the tightest cut that can be made with a 1/4” blade.  A dime is the size of the tightest curve that can be cut with a 3/16” blade.  A pencil eraser is the size of the tightest turn that you can make with a 1/8” blade.  After a while, you won’t even need an object to size the possible curve of a blade because you will have become familiar with this process.

There are options to matching the blade to the smallest curve pattern.  If there is only one very tight cut, it may be best to use a turning hole, a relief cut, successive passes or to change the blade.  If you have a lot of cutting to do, you can use a wider blade for bigger curves and then switch to a narrow blade for the tighter curves.  Changing blades can often save cutting and finish time.

Courtesy of Laguna Tools Inc.

# Band Saw			Name: ____________________

### Safety Test 						Date:  ______________

You must answer all questions correctly, or you will have to retake the test before you will be allowed to operate the band saw.

Safe or Unsafe (Indicate if the statement is SAFE or UNSAFE by printing the correct answer in the blank.)

- It is __________ to have someone else inside the safety zone

- It is __________ to talk to someone else while operating the band saw.

- It is __________ to allow your fingers or hands to be in line with the blade.

- It is __________ to avoid sharp turns that could bend and/or break the blade.

- It is __________ to remove loose clothing and jewelry, tie back long hair and roll up long sleeves before using the band saw.

- It is __________ to rush the cut and force the work piece into the saw, especially if you are in a hurry.

- It is __________ to ignore a strange noise and continue to use the saw.

- It is __________ to turn off the power and step back from the machine if the blade breaks.

- It is __________ to wait until the blade comes to a complete stop before removing any wood that is close to the blade.

- It is __________ to leave the band saw while the blade is moving.

- It is __________ to back out of a long cut or sharp curve with the machine running.

###### True or False  (Indicate if the statement is TRUE or FALSE by printing the correct answer in the blank.)

- _______ You must have the instructor’s permission before using the band saw.

- _______ Safety glasses are not required when using the band saw.

###### Multiple Choice  (Print the correct answer in the blank.)

- Adjust the blade guide assembly to within ________of the work piece				A. 3/4"    	B. 1/4"    	C. 1/2"   	D.  1"

15. Make _______cuts before cutting small radius curves.

A. Relief 	B. Saw  	C. Practice  	D.  Bevel

# Band Saw			Name: ANSWER KEY

### Safety Test 						Date:  ______________

You must answer all questions correctly, or you will have to retake the test before you will be allowed to operate the band saw.

Safe or Unsafe (Indicate if the statement is SAFE or UNSAFE by printing the correct answer in the blank.)

- It is    UNSAFE     to have someone else inside the safety zone

- It is    UNSAFE     to talk to someone else while operating the band saw.

- It is    UNSAFE     to allow your fingers or hands to be in line with the blade.

- It is  	SAFE 	      to avoid sharp turns that could bend and/or break the blade.

- It is  	SAFE 	      to remove loose clothing and jewelry, tie back long hair and roll up long sleeves before using the band saw.

- It is    UNSAFE     to rush the cut and force the work piece into the saw, especially if you are in a hurry.

- It is    UNSAFE     to ignore a strange noise and continue to use the saw.

- It is  	SAFE 	      to turn off the power and step back from the machine if the blade breaks.

- It is  	SAFE 	      to wait until the blade comes to a complete stop before removing any wood that is close to the blade.

- It is    UNSAFE     to leave the band saw while the blade is moving.

- It is    UNSAFE     to back out of a long cut or sharp curve with the machine running.

###### True or False  (Indicate if the statement is TRUE or FALSE by printing the correct answer in the blank.)

- TRUE	 You must have the instructor’s permission before using the band saw.

- FALSE	 Safety glasses are not required when using the band saw.

###### Multiple Choice  (Print the correct answer in the blank.)

- Adjust the blade guide assembly to within   1/4"  of the work piece					A. 3/4"    	B. 1/4"    	C. 1/2"   	D.  1"

15. Make  Relief cuts before cutting small radius curves.

A. Relief 	B. Saw  	C. Practice  	D.  Bevel