# Jointer

## Teacher Reference Page

Recommended Level(s) of use/Supervision

High School 		Independent student use (with permission)

Middle School	Direct Supervision ONLY (With instructor directly monitoring and assisting the individual student)

Elementary 		Teacher use only

Notes:

- Instructors may want to add additional items that are specific references to unique machines or circumstances in their specific lab.

- On questions 5 and 6, the instructor may want to add the dimension associated with their specific equipment.

- The parts identification sheet is optional that may be a required at your discretion.

- On Item #8 in the SAFETY RULES, then instructor may want to include a specific measure.

Safety Test:

- On question #15, the answer will depend on the instructors discretion, but it should never be less then the rated size of the jointer.  (NOTE:  This may also require an adjustment to the word bank.)

Reference:

# Jointer

### Safety Rules

- Always wear eye protection.

- Always ask the instructors permission before using the jointer.

- Always remove all jewelry and loose clothing and tie back long hair.

- Always keep the safety guard in place when using the jointer.

- Never put your hands directly over the cutter head when using the jointer.

- Never adjust the jointer when it is running.

- The normal depth of cut for general purpose edge jointing is 1/16”

- The normal depth of cut for face jointing is 1/32”.

- The minimum (shortest) length of wood that can be used is equal to the size of the jointer.

- The maximum width of stock that can be face jointed is equal to the size of the jointer.

- Never joint end grain on the jointer.

- Always use push blocks when face jointing the wood.

- Always use a push stick when edge jointing any piece that is less than the height of the fence.

- Never adjust the out feed table on the jointer in this lab.

# Jointer

### Operating Procedure

- You must pass the safety exam for the jointer.

- Ask the instructor’s permission to use the jointer

- Make sure you have safety glasses on.

- Be sure to remove all jewelry and loose fitting clothes and tie back long hair.

- Be sure that the wood meets the minimum length requirements for the jointer that you are using.

- Check the depth of cut.

- The usual depth of cut (amount of wood to remove each pass) for edge jointing is 1/16 of an inch: however, if the wood is badly warped or crowned adjust the depth to 1/8 of an inch.

- The usual depth of cut for face jointing is 1/32”: however if the wood is badly cupped or twisted adjust the depth to 1/16”.

- Check the fence to make sure that it is square.

- Turn the jointer on.

- Make sure that the grain is facing forward and up to avoid tear-out of the wood.

- When edge jointing:

- Place the top of the crown up.

- Always use a push stick on any piece of wood that is lower than the height of the fence.

- Be sure to hold the wood tightly against the fence at all times to ensure accurate results.

- When face jointing

- Be sure to place the convex surface of cupped stock so that it faces up.

- Always use push blocks when face jointing.

- Stand to the side of the machine and move with the stock as needed when jointing longer pieces.

- Turn the jointer off.

# Jointer				Name: ____________________

### Safety Test 						Date:  ______________

Write  Safe or Unsafe before each statement to make the sentence correct.

- It is __________ to always wear eye protection when using this machine.

- It is __________ to joint the end grain of the wood on this machine.

- It is __________ to leave the jointer when it is running.

- It is __________ to always use push blocks whenever you face joint stock.

- It is __________ to make any adjustments to the jointer when it is running.

- It is __________ to remove the safety guard or to hold the safety guard out of the way in order to get a better view of the wood.

- It is __________ to place your hands over the cutter head when edge jointing stock.

- It is __________ to set the jointer to remove ¼ of an inch during one pass when surface or edge jointing stock.

- It is __________  to make sure that your stock meets the minimum size requirements before jointing it.

- It is __________  to have an assistant help support long pieces of wood.

Fill in the blank- put in the word(s) to complete the statement

###### Word Bank

push stick		push block		infeed table		outfeed table 		depth		twist 		crown		jointer		height	      width

6”	8”	10”	12”	1/16”		¼”	½”	1/8”

- The minimum length of wood is equal to the  ______________ of the knives.

- The depth of cut for general-purpose work is  ________ of an inch per pass.

- A  ___________  _____________ should be used whenever edging narrow stock.

- The  _______________ should always face up when surfacing the wood.

- The minimum length of stock that may be jointed in this lab is __________ (specific dimension).

- You should never adjust the  ____________ ____________.

# Jointer				Name: ____________________

### Safety Test 						Date:  ______________

Write  Safe or Unsafe before each statement to make the sentence correct.

- It is     SAFE        to always wear eye protection when using this machine.

- It is _UNSAFE     to joint the end grain of the wood on this machine.

- It is _UNSAFE     to leave the jointer when it is running.

- It is __SAFE___  to always use push blocks whenever you face joint stock.

- It is _UNSAFE     to make any adjustments to the jointer when it is running.

- It is _UNSAFE     to remove the safety guard or to hold the safety guard out of the way in order to get a better view of the wood.

- It is _UNSAFE     to place your hands over the cutter head when edge jointing stock.

- It is _UNSAFE     to set the jointer to remove ¼ of an inch during one pass when surface or edge jointing stock.

- It is ___SAFE       to make sure that your stock meets the minimum size requirements before jointing it.

- It is ___SAFE       to have an assistant help support long pieces of wood.

Fill in the blank- put in the word(s) to complete the statement

###### Word Bank

  - push stick		push block		infeed table		outfeed table 		depth		twist 		crown		jointer		height	      width

  - 6”	8”	10”	12”	1/16”		¼”	½”	1/8”

- The minimum length of wood is equal to the   WIDTH   of the knives.

- The depth of cut for general-purpose work is  ___1/16”___ of an inch per pass.

- A  __PUSH       BLOCK    should be used whenever edging narrow stock.

- The         CROWN         should always face up when surfacing the wood.

- The minimum length of stock that may be jointed in this lab is   TEACHER SPECIFIED   (specific dimension).

- You should never adjust the  ___OUTFEED    TABLE__.

# Text boxes

- Base

- Guard

- Outfeed Table

- Fence

- Infeed Table

- Depth Adjustment Handwheel

- Depth Gage.