# Power Miter Saw

## Teacher Reference Page

Recommended Level(s) of use/Supervision

High School 		Independent student use (with permission)

Middle School	Independent student use (with permission)

Elementary 		Teacher use only

Notes:

- Instructors may want to add additional items that are specific references to unique machines or circumstances in their specific lab.

# Power Miter Saw

Safety Rules

- Always wear eye protection.

- Always ask the instructor before using the power miter saw

- Always remove jewelry, eliminate loose clothing and tie back long hair before operating the power miter saw.

- Always keep guards in place and in working order.

- Always remove all chips and small pieces of wood before operating saw.

- Always lock all adjustments before operating the saw.

- Always keep hands at least 5” from the path of the saw blade.

- Never cross your arms when using the power miter saw

- Never allow the blade to be in contact with the work piece before switching on machine.

- Always secure the work piece with your hand or a hold down clamp.

- Always wait until the blade has stopped completely before attempting to remove scraps.

- Never attempt to clear the sawdust chute unless the saw is unplugged.

# Power Miter Saw

### Operating Procedure

- Always Wear Safety Glasses when operating the Power Miter Saw!

- Always ask the instructor for permission before using the Power Miter Saw.

- Remove loose clothing and jewelry, tie back long hair and roll up long sleeves.

- Set the appropriate angle and lock the table in place.

- When cutting square or right-angled miters, hold piece of work with your left hand and operate the handle with your right hand.

- Never cross your arms when operating the power miter saw.

- Align the blade with your mark

- Without squeezing the power trigger, pull the blade down close to the stock.

- Adjust the stock so that the mark lines up with the blade.

- Return the saw to the fully upright position

- Squeeze the power trigger and wait for the blade to reach full speed before cutting.

- Pull the saw slowly and smoothly down through the work piece.

- Return the saw to its upright position and release the power trigger.

- Wait for the blade to come to a full stop before removing scraps.

- Return the saw to the straight and square position

- Tighten all adjustments.

# Power Miter Saw			Name: ____________

### Safety Test 						     	                        Date:  ________________

You must answer all questions correctly, or you will have to retake the test before you will be allowed to operate the power miter saw.

True or False (Indicate if the statement is True or False by printing the correct answer in the blank.)

- _______ It is safe to start your cut as soon as you pull the trigger.

- _______ You must have the instructor’s permission before using the Power Miter Saw.

- _______ Never attempt to clean the dust chute unless the saw is unplugged and you have         received permission from the instructor to do so.

- _______ Always make sure that the guard is in place and functioning properly.

- _______ Never talk to anyone while operating the power miter saw.

- _______ Always keep hands at least 5” from the path of the saw blade.

#### Fill in the blanks (PRINT the correct answer from the word bank in the blanks below)

- Make sure that the __________ is not in contact with the work piece before switching on machine.

- For your safety remove all _________ and small pieces of __________ before operating saw.

- Lock __________ in position before cutting any stock.

- When cutting square or right angled miters, hold the stock with your ________ hand and operate the saw with your ________ hand.

- Always wait until the _________ has stopped completely before attempting to remove scraps.

# Power Miter Saw			Name: Answer Key

### Safety Test 						     	                        Date:  ________________

You must answer all questions correctly, or you will have to retake the test before you will be allowed to operate the power miter saw.

True or False (Indicate if the statement is True or False by printing the correct answer in the blank.)

- ___F____ It is safe to start your cut as soon as you pull the trigger.

- ___T____ You must have the instructor’s permission before using the Power Miter Saw.

- ___T____ Never attempt to clean the dust chute unless the saw is unplugged and you have         received permission from the instructor to do so.

- ___T____ Always make sure that the guard is in place and functioning properly.

- ___T____ Never talk to anyone while operating the power miter saw.

- ___T____ Always keep hands at least 5” from the path of the saw blade.

#### Fill in the blanks (PRINT the correct answer from the word bank in the blanks below)

- Make sure that the __Blade_____ is not in contact with the work piece before switching on machine.

- For your safety remove all _Wood____ and small pieces of _Scraps___ before operating saw.

- Lock _Table____ in position before cutting any stock.

- When cutting square or right angled miters, hold the stock with your _Left___ hand and operate the saw with your _Right__ hand.

- Always wait until the __Blade__ has stopped completely before attempting to remove scraps.

# Text boxes

Word Bank

Left		Guard		Right		Wood		Table		Scraps

Stock		Door		Handle	Blade

Word Bank

Left		Guard		Right		Wood		Table		Scraps

Stock		Door		Handle	Blade

Bevel Lock Handle

Bevel Gauge

Fence

Miter Lock Handle

Miter Gauge

Saw Guard