# Scroll saws

## Teacher Reference Page

Recommended Level(s) of use/Supervision

High School 		Independent student use (with permission)

Middle School	Independent student use (with permission)

Elementary 		Teacher use only

Notes:

- Instructor may want to add specific information regarding blade changes as they pertain to their specific lab procedures.

- Instructors may want to add additional items that are specific references to unique machines or circumstances in their specific lab.

# Scroll saws

### Safety Rules

- Always ask the instructors permission before using the scroll saw.

- Always were safety glasses when operating the scroll saw.

- Always remove jewelry, eliminate loose clothing and tie back long hair before operating the scroll saw.

- Always check the setup and adjustments before turning on the saw.

- Blade Tension

- Teeth on blade pointing down.

- Hold down should be lightly touching the work.

- Never make any adjustments when the saw is running. (The only exception is speed adjustments on electronic or crank operated variable speed models)

- Never talk to anyone while operating the scroll saw.

- Never allow another student inside the safety zone.

- Always keep hands and fingers on either side of the cut line

- Never place hands or fingers inline with the blade.

- Immediately shut off the machine if the blade breaks or if any strange noise is heard and inform the teacher.

- Never force the cut.

# Scroll saws

### Operating Procedure

- You must pass the safety exam for the scroll saw at 100%.

- Ask the instructor’s permission to use the scroll saw.

- Remove loose clothing and jewelry, tie back long hair and roll up long sleeves.

- Make sure that the appropriate blade is in the saw (a narrow blade for tight curves)

- Adjust the hold down foot so that it is lightly touching your work piece.

- Make sure that no other students are within the safety zone.

- Turn the saw on.

- Adjust the speed as required (only applies to variable speed models as indicated by the instructor).

- Use moderate pressure to hold the work piece against the table (do not allow the work piece to bounce)

- Slowly cut along your cut line.

- Allow the saw to do the work, DO NOT FORCE!

- When finished, turn the saw off.

- Clear away all scraps AFTER the saw has come to a complete stop.

# Scroll saws			Name: ____________________

### Safety Test 						Date:  ______________

You must answer all questions correctly, or you will have to retake the test before you will be allowed to operate the scroll saws.

True or False (Indicate if the statement is TRUE or FALSE by printing the correct answer in the blank.)

- _______	You must always ask the instructors permission to use the scroll saws.

- _______	It is Unsafe to make adjustments to the scroll saws when it is running.

- _______	It is Safe to operate the scroll saws without wearing safety glasses.

- _______	It is Unsafe to place your hands or fingers on the cut line.

- _______	If the scroll saws makes a strange noise or the blade breaks, shut the saw off immediately and notify the instructor.

- _______	It is Safe to allow another student inside the safety zone when operating the scroll saws.

- _______	Always remove jewelry, eliminate loose clothing, and tie back long hair before operating the scroll saws.

- _______	It is Unsafe to talk to someone when operating the scroll saws.

- _______	It is Safe to force your stock into the blade when cutting on the scroll saw.

- _______	It is safe to allow the workpiece to bounce on the table when cutting on the scroll saws

Multiple Choice  (Print the correct answer in the blank.)

- The hold down foot should be __________  __________ the work?

A.  Jammed against		B. slightly above	  	C. lightly touching

# Scroll saws			Name: Answer Key

### Safety Test 						Date:  ______________

You must answer all questions correctly, or you will have to retake the test.  Print neatly and be specific in your answers.

True or False (Indicate if the statement is TRUE or FALSE by printing the correct answer in the blank.)

- True	You must always ask the instructors permission to use the scroll saws.

- True	It is Unsafe to make adjustments to the scroll saws when it is running.

- False	It is Safe to operate the scroll saws without wearing safety glasses.

- True	It is Unsafe to place your hands or fingers on the cut line.

- True	If the scroll saws makes a strange noise or the blade breaks, shut the saw off immediately and notify the instructor.

- False	It is Safe to allow another student inside the safety zone when operating the scroll saws.

- True	Always remove jewelry, eliminate loose clothing, and tie back long hair before operating the scroll saws.

- True	It is Unsafe to talk to someone when operating the scroll saws.

- False	It is Safe to force your stock into the blade when cutting on the scroll saw.

- False	It is safe to allow the workpiece to bounce on the table when cutting on the scroll saws

Multiple Choice  (Print the correct answer in the blank.)

- The hold down foot should be lightly touching the work?

A.  Jammed against		B. slightly above	  	C. lightly touching